## Slide 1: General-purpose I/Os (GPIO)

## Slide 2: STM32F407G-DISC1 Discovery

## Slide 3: STM32F407xx package information

## Slide 4: Key features

## Slide 5: GPIO main features
• Up to 16 I/Os under control
• Output states: push-pull or open drain + pull-up/down
• Input states: floating, pull-up/down, analog
• Analog function
• Alternate function input/output selection registers (at most 16 AFs per I/O)
• Fast toggle capable of changing every two clock cycles
• Highly flexible pin multiplexing allows the use of I/O pins as GPIOs or as one of several
peripheral functions

## Slide 6: GPIO functional description
• Input floating
• Input pull-up
• Input-pull-down
• Analog
• Output open-drain with pull-up or pull-down capability
• Output push-pull with pull-up or pull-down capability
• Alternate function push-pull with pull-up or pull-down capability
• Alternate function open-drain with pull-up or pull-down capability

## Slide 7: Basic structure of a five-volt tolerant I/O port bit

## Slide 8: Input configuration
The output buffer is disabled
The Schmitt trigger input is activated
The pull-up and pull-down resistors are activated depending on the value in the GPIOx_PUPDR register
The data present on the I/O pin are sampled into the input data register every AHB1 clock cycle

## Slide 9: Output configuration
The output buffer is enabled:
– Open drain mode: A “0” in the Output register activates the N-MOS whereas a “1” in the Output register leaves the port in Hi-Z (the P-MOS is never activated)
– Push-pull mode: A “0” in the Output register activates the N-MOS whereas a “1” in the Output register activates the P-MOS
• The Schmitt trigger input is activated
• The weak pull-up and pull-down resistors are activated or not depending on the value in the GPIOx_PUPDR register
• The data present on the I/O pin are sampled into the input data register every AHB1 clock cycle
• A read access to the input data register gets the I/O state
• A read access to the output data register gets the last written value

## Slide 10: Alternate function

## Slide 11: Alternate function configuration
The output buffer can be configured as open-drain or push-pull
The output buffer is driven by the signal coming from the peripheral (transmitter enable and data)
The Schmitt trigger input is activated
The weak pull-up and pull-down resistors are activated or not depending on the value in the GPIOx_PUPDR register
The data present on the I/O pin are sampled into the input data register every AHB1 clock cycle
A read access to the input data register gets the I/O state

## Slide 12: Special considerations for I/O pins

## Slide 13: Special considerations for HSE/LSI pins

## Slide 14: Analog configuration
The output buffer is disabled
The Schmitt trigger input is deactivated, providing zero consumption for every analog
value of the I/O pin. The output of the Schmitt trigger is forced to a constant value (0).
The weak pull-up and pull-down resistors are disabled
Read access to the input data register gets the value “0”

## Slide 15: Структура для настройки порта
typedef struct
{
uint32_t GPIO_Pin; /*!< Specifies the GPIO pins to be configured.
GPIOMode_TypeDef GPIO_Mode; /*!< Specifies the operating mode for the selected pins.
GPIOSpeed_TypeDef GPIO_Speed; /*!< Specifies the speed for the selected pins.
GPIOOType_TypeDef GPIO_OType; /*!< Specifies the operating output type for the selected pins.
GPIOPuPd_TypeDef GPIO_PuPd; /*!< Specifies the operating Pull-up/Pull down for the selected pins.
}GPIO_InitTypeDef;

## Slide 16: GPIO_Mode
typedef enum
{
GPIO_Mode_IN = 0x00, /*!< GPIO Input Mode */
GPIO_Mode_OUT = 0x01, /*!< GPIO Output Mode */
GPIO_Mode_AF = 0x02, /*!< GPIO Alternate function Mode */
GPIO_Mode_AN = 0x03 /*!< GPIO Analog Mode */
}GPIOMode_TypeDef;

## Slide 17: GPIO_Speed
typedef enum
{
GPIO_Speed_2MHz = 0x00, /*!< Low speed */
GPIO_Speed_25MHz = 0x01, /*!< Medium speed */
GPIO_Speed_50MHz = 0x02, /*!< Fast speed */
GPIO_Speed_100MHz = 0x03 /*!< High speed on 30 pF (80 MHz Output max speed on 15 pF) */
}GPIOSpeed_TypeDef;

## Slide 18: GPIO_OType
typedef enum
{
GPIO_OType_PP = 0x00,
GPIO_OType_OD = 0x01
}GPIOOType_TypeDef;

## Slide 19: GPIO_PuPd
typedef enum
{
GPIO_PuPd_NOPULL = 0x00,
GPIO_PuPd_UP = 0x01,
GPIO_PuPd_DOWN = 0x02
}GPIOPuPd_TypeDef;

## Slide 20: GPIO_Init
void LED_Init(void)
{
GPIO_InitTypeDef GPIO_InitStruct; //Структура для настройки порта
RCC_AHB1PeriphClockCmd(RCC_AHB1Periph_GPIOD, ENABLE); //Включаем тактирование порта GPIOD
GPIO_InitStruct.GPIO_Pin = GPIO_Pin_12; //Указываем, что настраиваем вывод D12
GPIO_InitStruct.GPIO_Mode = GPIO_Mode_OUT; //Указываем, что используем его как выход
GPIO_InitStruct.GPIO_Speed = GPIO_Speed_50MHz; //Указываем скорость порта (50 МГц)
GPIO_InitStruct.GPIO_OType = GPIO_OType_PP; //Указываем тип порта как двухтактный
GPIO_InitStruct.GPIO_PuPd = GPIO_PuPd_NOPULL; //Указываем, что подтяжка не нужна
GPIO_Init(GPIOD, &GPIO_InitStruct);
GPIO_ResetBits(GPIOD, GPIO_Pin_12); //Устанавляваем вывод 12 порта в нуль
}